## Slide 1: PASTRY & BAKERY EQUIPMENTS AND UTENSILS

## Slide 2: LARGE EQUIPMENT Mixers, ovens, and dough-handling equipment take up most of this category.
Vertical Mixer
Also called planetary mixer, this is the most common type of mixer used in baking as well as in cooking. The term planetary is descriptive of the motion of the beater attachment. Just as a planet spins on its own axis while revolving around the sun, so the beater attachment spins on its axis while it rotates in an orbit to reach all parts of the stationary bowl. Tabletop mixers range in capacity from 5 to 20 qt (4.75 to 19 L). Floor models are available as large as 140 qt (132 L).

## Slide 3: Vertikal Mixer
Vertical mixers have three main mixing attachments.
The paddle is a flat blade used for general mixing.
The wire whip is used for such tasks as beating egg foams and cream.
The dough arm or dough hook is used for mixing and kneading yeast doughs.
Be sure to use the right size attachment for the bowl.
Mixer attachments: (left) whip, (center) paddle,(right) dough arm

## Slide 4: Others Mixer
Spiral Mixer
Spiral mixers are designed for doughs and heavy batters and are used primarily for making large quantities of yeast doughs for breads and bagels.
Horizontal Mixer
Horizontal mixers are large, industrial-size mixers capable of handling as much as several thousand pounds of dough at a time. Each model is designed to work best with a specific range of products, such as bread doughs, pastry doughs, or soft doughs and batters.

## Slide 5: DOUGH-HANDLING EQUIPMENT
Divider-Rounder
This machine divides the dough as does a simple divider, and it then automatically rounds the individual portions, greatly speeding makeup of the dough products.
Dough Sheeter
A sheeter rolls out portions of dough into sheets of uniform thickness. It consists of a canvas conveyor belt that feeds the dough through a pair of rollers. To make thin sheets, the dough usually must be passed back and forth through the rollers several times. The operator decreases the space between the rollers after each pass.

## Slide 6: DOUGH-HANDLING EQUIPMENT
Proofer
A proofer is a special box used to create the ideal conditions for fermenting yeast doughs. It does this by maintaining a preset warm temperature and humidity level appropriate to the specific dough.
Retarder
Chilling or refrigerating yeast dough slows down or retards the rate of fermentation so the dough can be stored for later baking. A retarder is a refrigerator that maintains a high level of humidity to prevent the dough from drying out or crusting

## Slide 7: OVENS
Deck Oven
Deck ovens are so called because the items to be baked—either on sheet pans or, in the case of some breads, freestanding are placed directly on the bottom, or deck, of the oven. There are no racks for holding pans in deck ovens.
Rack Oven
A rack oven is a large oven into which entire racks full of sheet pans can be wheeled for baking. Normal baker’s racks may hold from 8 to 24 full-size sheet pans, but racks made specifically to go into rack ovens usually hold about 15 to 20 pans. Rack ovens hold one to four of these racks at once. These ovens are also equipped with steam injectors.

## Slide 8: OVENS
Mechanical Oven
In a mechanical oven, the food is in motion while it bakes. The most common type is a revolving oven
This mechanical action eliminates the problem of hot spots or uneven baking because the mechanism rotates the foods throughout the oven.
Convection Oven
Convection ovens contain fans that circulate the air and distribute the heat rapidly throughout the interior. The forced air makes foods cook more quickly at lower temperatures. Because the strong forced air can distort the shape of items made with batters and soft doughs, and because the air may be strong enough to blow baking parchment off sheet pans,

## Slide 9: DOUGH-HANDLING EQUIPMENT
FRYER
Fryers are needed for doughnuts and other fried items. Small operations often use standard deep fryers (or even stovetop kettles), but larger doughnut fryers are best if you make doughnuts in quantity.
Ice Cream Machine
An ice cream maker has to simultaneously freeze the mixture while churning it so as to aerate the mixture and avoid ice crystals. As a result, most ice creams are ready to consume immediately. However, those containing alcohol must often be chilled further to attain a firm consistency.

## Slide 10: DOUGH-HANDLING EQUIPMENT
Heavy Duty Scale
Used for measuring the exact heavy quality of items and ingredients.
Trolley Sheet Pan

## Slide 11: Working table
Marble Slab/ Marble Table
Used for chocolate tempering, sugar modeling and fondant making.
Stainless Steel Working Table
Used for preparing food and used in the pastry & bakery area

## Slide 12: Baking Materials
Baking Sheet Pan
Baking sheets are rimless, flat metal sheets. They normally have a small rim on the short sides for easy gripping.
Baking / Cake Tin
Sizes 18 cm until 30 cm in diameter. The pans should be at least 5 until 6 cm

## Slide 13: Baking Materials
Cake / Baking Form
Loaf pans are used for most quick bread recipes or baking cakes, such as banana cake, butter cake and Sweat bread or even for open sandwich bread
Cupcake/Muffin Pans
Cupcake and Muffin pans are a rectangular metal baking pan with six or twelve cup, used to bake both muffins and cupcakes. Muffin pan sizes are typically mini, standard, and jumbo sized. A standard muffin pan has 12 cups

## Slide 14: Baking Materials
Gugelhopf Pans
Gugelhopf pans are for baking Gugelhopf, A European cake baked in a special Kugelhopf pan which is a deep, round, tube pan with ornate fluting, and a narrow center tub
Metal Pie Pans
Used for baking pies such as fruit pies and meat pies and baking cakes such as nut chocolate cake, hollandaise cake

## Slide 15: Baking Materials